Computer Organisation and Architecture

Unit 1:
Introduction

Unit 2:
CPU Design and Peripheral Devices

Unit 3:
Pipelining

Unit 4:
Memory Organisation

______________________________________________________________________

Unit 1:
Introduction to computer organisation and architecture

What is computer architecture:
- The description of all the functions of the units of digital computer.

What is computer organisation:
-

Basically:
Architecture is WHAT a computer does (high level)
Organisation is HOW a computer does (low level)

Von-Neumann/Princeton:
- Program and data memory same
- Single bus
- Instruction fetch and data transfer can’t be simultaneous

Harvard:
- Separate program and data memory
- Separate buses for program and data memory
- Instruction fetch and data transfer can be same time
- Modified Harvard: separate cache memory but same main memory.

Outline:

CPU (central processing unit)

carries out all the instructions given by a program.

Has the following elements:
- Register set (intermedieate data)
- ALU (arithmetic and logical unit) (micro-operations)
- Control unit (supervises the processes)

Main memory:

RAM(Rendom access memory):
- DRAM (dynamic RAM) (slow & cheap) {main mem}
- SRAM (static RAM) (fast & expensive) {cache}

ROM(Read only memory) (non-volatile)
- PROM (Programmable ROM) (one time)
- EPROM (Erasable PROM) (erasable by UV light)
- EEPROM (Electronically EPROM) (electronically erasable)

Secondary memory:
- HDD (slow, large capacity)
- SSD (fast, expensive)
- Optical drive (CD, DVD, Blu-ray)
- Magnetic tapes

General Register Organisation:
A set of flip flops forms a register. A register is a unique high-speed storage area in the CPU.
- Memory locations are needed for storing data like pointers, counters, adresses, return address, temporary result etc. Having to refor to memory location of such applications is time consuming because memory access is the most time consuming operation in the computer.
- It is more conveinent and more efficient to store thense intermediate values in processor registers. All of these registers are connect to a common bus system.
- The register communicate wich each other net only for direct data transfer but also while performing various microoperations.
- When large number of register included in the CPU then it is more efficient to connect through common bus system.