Computer Organisation and Architecture

Unit 1:
Introduction

Unit 2:
CPU Design and Peripheral Devices

Unit 3:
Pipelining

Unit 4:
Memory Organisation

______________________________________________________________________

Unit 1:
Introduction to computer organisation and architecture

What is computer architecture:
- The description of all the functions of the units of digital computer.

What is computer organisation:
-

Basically:
Architecture is WHAT a computer does (high level)
Organisation is HOW a computer does (low level)

Von-Neumann/Princeton:
- Program and data memory same
- Single bus
- Instruction fetch and data transfer can’t be simultaneous

Harvard:
- Separate program and data memory
- Separate buses for program and data memory
- Instruction fetch and data transfer can be same time
- Modified Harvard: separate cache memory but same main memory.

Outline:

CPU (central processing unit)

carries out all the instructions given by a program.

Has the following elements:
- Register set (intermedieate data)
- ALU (arithmetic and logical unit) (micro-operations)
- Control unit (supervises the processes)

Main memory:

RAM(Rendom access memory):
- DRAM (dynamic RAM) (slow & cheap) {main mem}
- SRAM (static RAM) (fast & expensive) {cache}

ROM(Read only memory) (non-volatile)
- PROM (Programmable ROM) (one time)
- EPROM (Erasable PROM) (erasable by UV light)
- EEPROM (Electronically EPROM) (electronically erasable)

Secondary memory:
- HDD (slow, large capacity)
- SSD (fast, expensive)
- Optical drive (CD, DVD, Blu-ray)
- Magnetic tapes

General Register Organisation:
A set of flip flops forms a register. A register is a unique high-speed storage area in the CPU.
- Memory locations are needed for storing data like pointers, counters, adresses, return address, temporary result etc. Having to refor to memory location of such applications is time consuming because memory access is the most time consuming operation in the computer.
- It is more conveinent and more efficient to store thense intermediate values in processor registers. All of these registers are connect to a common bus system.
- The register communicate wich each other net only for direct data transfer but also while performing various microoperations.
- When large number of register included in the CPU then it is more efficient to connect through common bus system.

Digital Electronics:
Number systems:
- Binary (base 2) (0-1)
- Octal (base 8) (0-7)
- Decimal (Base 10) (0-9)
- Hexadecimal (Base 16) (0-F)

Basic Gates:
- AND Gate
- OR Gate
- NOT Gate

Universal Gates:
- NAND Gate
- NOR Gate

Logic Gates:
- All of the above
- XOR Gate
- XNOR Gate

AND Gate: | OR Gate: | NOT Gate:
X | Y | Out | X | Y | Out | X | Out
0 | 0 | 0 | 0 | 0 | 0 | 0 | 1
0 | 1 | 0 | 0 | 1 | 1 | 1 | 0
1 | 0 | 0 | 1 | 0 | 1 |
1 | 1 | 1 | 1 | 1 | 1 |
---------------+-----------------+------------------
NAND Gate: | NOR Gate: | XOR Gate:
X | Y | Out | X | Y | Out | X | Y | Out
0 | 0 | 1 | 0 | 0 | 1 | 0 | 0 | 0
0 | 1 | 1 | 0 | 1 | 0 | 0 | 1 | 1
1 | 0 | 1 | 1 | 0 | 0 | 1 | 0 | 1
1 | 1 | 0 | 1 | 1 | 0 | 1 | 1 | 0
---------------+-----------------+------------------
XNOR Gate: |
X | Y | Out |
0 | 0 | 1 |
0 | 1 | 0 |
1 | 0 | 0 |
1 | 1 | 1 |

AND + NOT = NAND
OR + NOT = NOR
XOR + NOT = XNOR

Case 1:
A | B | Out
0 | 0 | 0
0 | 1 | 0
1 | 0 | 0
1 | 1 | 1

Case 2:
A | B | Out
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1

Conversion of number system:

Converting decimal to binary:

keep diving the dividend by 2 and store the remainders in a stack.
The stack, read top to down will read the equivalent binary form of the number. e.g.

42 / 2 = 21 remainder 0
21 / 2 = 10 remainder 1
10 / 2 = 5 remainder 0
5 / 2 = 2 remainder 1
2 / 2 = 1 remainder 0
1 / 2 = 0 remainder 1

Therefore (42)10 = (101010)2

Converting binary to decimal:

multiply each place with powers of two, starting from 0 going from right to left and add all the numbers together.

Converting octal to binary:

just replace each digit with it’s binary representation:

Converting binary to octal:

group the elements into groups of three and replace each group by it’s octal equivalent.

Converting Hexadecimal to binary:

again, replace each digit with it’s binary representation.

Converting binary to hexadecimal:

group the elements into groups of four and replace each group by it’s hexadecimal equivalent.

Law of Boolean Algebra:

And law:

A.A = A
A.1 = A
A.0 = 0
A.!A= 0

Or law:

A+A = A
A+1 = 1
A+0 = A
A+!A= 1

Commutative law:
A+B = B+A

Distributive law:
A(B+C) = A.B + A.C
A+BC = (A+B)(A+C)